## Slide 1: ENGR 1111 Intro to Engineering: Civil Engineering Fall 2022 Part 8: Risk Assessment

## Slide 2
Objectives
  Concept or perception of risk
  How to calculate risk
  The steps involved in performing risk assessments
  Environmental impact statements
Part 8: Risk Assessment

## Slide 3
Concept or Perception of Risk:
Part 8: Risk Assessment

## Slide 4
Concept or Perception of Risk:
Part 8: Risk Assessment

## Slide 5
Concept or Perception of Risk:
  Risk vs Safety:
    Risk – probability that an adverse effect or outcome will occur
    Safety – probability that no adverse effect will occur
  Risk:
    Expressed numerically and has no units
    Reported as a fraction between 0 and 1 or as a percentage
    The closer risk is to 1, the higher the probability of the event happening
    May be calculated as lifetime risk or annual risk
Part 8: Risk Assessment

## Slide 6
Risk Assessment:
  Risk is a function of hazards and exposures
  Hazard – anything that produces an adverse effect on human health and the environment or ecosystem
  Exposure – qualitative or quantitative assessment of contact to the skin or body by a chemical
Part 8: Risk Assessment

## Slide 7
Data Collection and Evaluation
Toxicity Assessment
Exposure Assessment
Risk Characterization
Risk Management
Part 8: Risk Assessment

## Slide 8
Data Collection and Evaluation
  Baseline Risk Assessment Data
    Identification of potential contaminants
    Concentration of contaminants
    Characterization of sources and environmental setting
  Develop a Sampling Plan
    A sampling plan will reflect background levels of naturally occurring and anthropogenic levels of chemicals
Part 8: Risk Assessment
    Environmental Protection Agency’s Environmental Sampling and Analytical Methods Program

## Slide 9
Toxicity Assessment
  Toxicity involves studying the adverse effects of exposure of living organisms to chemicals or toxicants
  The result of exposure depends on an individual’s susceptibility
    Factors that affect susceptibility:
      Gender
      Age
      Diet
      Genetics
      Prior Exposure
Part 8: Risk Assessment

## Slide 10
Toxicity Assessment
  The toxicity component of the baseline risk assessment considers:
    Types of adverse health effects associated with the exposure to specific chemicals
    The relationship between the magnitude of exposure and adverse effects
    Related uncertainties of a compound’s cancer-causing ability (carcinogenicity) to humans
Part 8: Risk Assessment

## Slide 11
Toxicity Assessment
  Hazard Identification – process of determining whether exposure to a toxicant is linked to a particular health effect (examples: cancer, birth defects, etc.)
    Many times, studies are conducted on animals or tissue. These studies are called bioassays
  Toxicants can promote acute toxicity (short period of time) or chronic toxicity (long term exposure)
    Chronic toxicity may result in mutation of genetic material
  Carcinogens – toxicants capable of causing cancer
  Teratogens – toxicants capable of causing birth defects
Part 8: Risk Assessment

## Slide 12
Toxicity Assessment
  Dose-response Assessment – process of evaluating the relationship between the level of exposure to the toxicant and the extent of adverse effect on the individual
    Carcinogenic or noncarcinogenic
    Acute or chronic
  Dose – mass of a chemical received by the exposed individual, expressed in milligrams per kilogram (mg/kg) of body weight
Part 8: Risk Assessment

## Slide 13
Toxicity Assessment
  The quantity of a specific chemical required to kill an organism normally follows a S-shaped curve
  The dose at which 50% of the organisms die is the median lethal dose (LD50)
Part 8: Risk Assessment

## Slide 14
Toxicity Assessment
  Instead of mortality, the response may be reported as the probability or risk of causing cancer
Part 8: Risk Assessment

## Slide 15
Toxicity Assessment
  Noncarcinogenic effects
    Lowest-observed-adverse-effect level (LOAEL) – lowest dose administered that elicits an adverse response
    No-observable-adverse-effect level (NOAEL) – highest dose administered that does not create an adverse effect
    Reference dose (RfD) – generally estimated by
Part 8: Risk Assessment
    dividing the NOAEL by an uncertainty factor of 10 (minimal uncertainty), 100, or 1000 (less certainty)

## Slide 16
Part 8: Risk Assessment

## Slide 17
Toxicity Assessment
  Mathematical Modeling of Dose-Response Curves
    One-hit model
      Assumes that a single chemical or toxicant will result in the formation of a tumor in the exposed individual
    Multi-stage model
      Based on the multistage formation of tumors that is caused by a sequence of events
  The Environmental Protection Agency uses a multi-stage model called the linearized multistage model that assumes a linear relationship between risk and dose at low doses
    Slope factor (SF) – slope of the dose-response curve
Part 8: Risk Assessment

## Slide 18
Toxicity Assessment
  Slope Factor
    Where,
      Slope factor = slope of dose-response curve, (kg*day)/mg
      Incremental Lifetime Cancer Risk = incremental risk of cancer in a lifetime above the background rate, dimensionless
      Chronic Daily Intake (CDI) = the average dose of toxicant absorbed per kilogram of body weight over an entire lifetime, (70 years), mg/(kg*day)
Part 8: Risk Assessment

## Slide 19
Toxicity Assessment
Part 8: Risk Assessment

## Slide 20
Exposure Assessment
  A toxicant can enter the body by:
    Inhalation - air
    Ingestion – food and liquids
    Absorption
  Exposure media:
    Surface water
    Groundwater
    Sediment
    Air
    Soil and dust
    Food
Part 8: Risk Assessment

## Slide 21
Exposure Assessment
  Evaluating toxicant releases
  Identifying exposed populations and potential pathways
  Estimating exposure-point toxicant concentrations
  Estimating toxicant intakes for specific pathways
  Exposure Period
    Acute (1 day)
    Subacute (10 days)
    Subchronic (2 weeks to 7 years)
    Chronic (7 years to lifetime)
Part 8: Risk Assessment

## Slide 22
Exposure Assessment
  Generic equation for estimating chronic daily intake (CDI)
Part 8: Risk Assessment

## Slide 23
Exposure Assessment
  Reasonable Maximum Exposure (RME) is determined by the EPA
Part 8: Risk Assessment

## Slide 24
Exposure Assessment
Part 8: Risk Assessment

## Slide 25
Exposure Assessment
Part 8: Risk Assessment

## Slide 26
Exposure Assessment
Part 8: Risk Assessment

## Slide 27
Risk Characterization
  Carcinogens
Part 8: Risk Assessment

## Slide 28
Risk Characterization
  Noncarcenogenics
    EPA uses a hazard index for noncarcinogenic compounds
    When more than one non-carcinogenic compound is present, the sum of HIs is determined.
    A hazard index of less than 1.0 is acceptable
Part 8: Risk Assessment

## Slide 29
Risk Characterization
Part 8: Risk Assessment

## Slide 30: ENGR 1111 Intro to Engineering: Civil Engineering Fall 2022 Part 8: Risk Assessment