## Slide 1: ENGR 1111 Intro to Engineering: Civil Engineering Fall 2022 Part 7: Environmental Engineering Calculations

## Slide 2
Objectives
  Units and Dimensions
  Units of Concentration for Liquid and Gas Phases
  Density
  Concept of Flow Rate and Residence Time
  Precision and Accuracy
Part 7: Environmental Engineering Calculations

## Slide 3
Why are units important?
  A number without units has no meaning in engineering
  A number with improper units has a misleading meaning
Example:
  1999 Mars Climate Orbiter
    Launched in December 1998, communication lost in September 1999
    Measurement mismatch failure
    NASA used metric while the manufacturer used US customary units
Part 7: Environmental Engineering Calculations

## Slide 4
Dimensions – used to describe the measurable aspects of an object
Units – increments necessary to quantify dimensions
Common dimensions:
  Length
  Mass
  Time
  Temperature
Derived units:
  Volume
  Density
  concentration
Part 7: Environmental Engineering Calculations

## Slide 5
Part 7: Environmental Engineering Calculations

## Slide 6
Part 7: Environmental Engineering Calculations

## Slide 7
Part 7: Environmental Engineering Calculations

## Slide 8
Part 7: Environmental Engineering Calculations

## Slide 9
Part 7: Environmental Engineering Calculations

## Slide 10
Significant Figures
  Measurements are uncertain, therefore only meaningful numbers are used.
  Three rules in determining significant figures:
    Non-zero digits are always significant.
    Any zeros between two significant digits are significant.
    A final zero or trailing zeros in the decimal portion ONLY are significant.
Part 7: Environmental Engineering Calculations

## Slide 11
Significant Figures
  Non-zero digits are always significant.
    How many significant figures are in the following?
      25.74 – 4 sig figs
      66.4 – 3 sig figs
      7.3 – 2 sig figs
      12.5 – 3 sig figs
Part 7: Environmental Engineering Calculations

## Slide 12
Significant Figures
  Any zeros between two significant digits are significant.
    Given the number 406, how many numbers are significant?
    4 and 6 are significant by the first rule
    To make a measurement decision on the 4 (in the hundred’s place) and the 6 (in the unit's place), a decision has to be made on the ten's place. The measurement scale for this number would have hundreds and tens marked with an estimation made in the unit's place.
Part 7: Environmental Engineering Calculations

## Slide 13
Significant Figures
A final zero or trailing zeros in the decimal portion ONLY are significant.
    How many significant figures are in the following?
      0.00600 – 3 sig figs
      0.03040 – 4 sig figs
      2.50x10-5 – 3 sig figs
      4.300x1014 – 4 sig figs
Part 7: Environmental Engineering Calculations

## Slide 14
Significant Figures
Addition and Subtraction
    Count the number of significant figures in the decimal portion of each number in the problem.
    Add or subtract in the normal fashion.
    Round the answer to the LEAST number of places in the decimal portion of any number in the problem.
Part 7: Environmental Engineering Calculations

## Slide 15
Significant Figures
Multiplication and Division
    The LEAST number of significant figures in any number of the problem determines the number of significant figures in the answer.
Part 7: Environmental Engineering Calculations

## Slide 16
Density – the ratio of mass to a unit volume
  Where,
    r = density, kg/m3
    m = mass, kg
    V = volume, m3
Part 7: Environmental Engineering Calculations
Density is independent of sample size but varies with temperature or the concentration of impurities
Example: saltwater vs fresh water

## Slide 17
Part 7: Environmental Engineering Calculations

## Slide 18
  Example 1:
    A 2 L graduated cylinder initially contains 500 ml of water. An irregularly shaped object having a mass of 105 g is submerged into the water. The final volume of the water in the cylinder is 1025 ml. Determine the density of the object.
Part 7: Environmental Engineering Calculations

## Slide 19
  Example 2:
    During an environmental assessment of a natural wetland in the Everglades, it was determined that 1.5 cubic meters of the dry native soil had a mass of 420 kg. Determine the mass of a cubic foot of that same soil.
Part 7: Environmental Engineering Calculations

## Slide 20
Concentrations – a concentration of a substance dissolved in a liquid are often described on a mass-per-unit-volume basis
  Where,
    C = concentration of dissolved substance, mg/L
    m = mass of solute or dissolved substance, mg
    V = total volume, L
Part 7: Environmental Engineering Calculations

## Slide 21
Part 7: Environmental Engineering Calculations
Mass-per-unit-mass basis
The most common mass-based units are parts per million (ppm) and parts per billion (ppb).
For perspective, the maximum contaminant level goal (MCLG) of mercury in drinking water allowed by the Environmental Protection Agency (EPA) is 0.002 ppm. This means that there can be no more than 0.002 grams of mercury in every million grams of drinking water purified and distributed by your local municipality.
Assuming the density of water is 1.0 g/ml, this is equivalent to allowing only 2 grams of mercury in approximately 264,000 gallons of drinking water.

## Slide 22
  Example 3:
    In many environmental aqueous systems, it is appropriate to make the simplifying assumption that 1 mg/L is equal to 1 ppm, provided that the fluid in question is primarily water, so that the density of the solution is essentially 1 g/ml. Show that 1 mg/L = 1 ppm.
Part 7: Environmental Engineering Calculations

## Slide 23
Molarity (M = moles per liter) – one mole per unit volume of substance
  Avogadro’s number defines a mole (mol)
    6.02 x 1023 molecules of any material per mole
  The atomic mass of an element or substance is equal to the mass of one mole of that substance
Part 7: Environmental Engineering Calculations

## Slide 24
Mass Percent and Volume Percent
  Mass percent of species A:
  Where,
    M A = mass of compound A, lbm (g)
    M A + M A = total mass of the solution, lbm (g)
Part 7: Environmental Engineering Calculations

## Slide 25
Mass Percent and Volume Percent
  Volume percent of species A:
Part 7: Environmental Engineering Calculations

## Slide 26
  Example 4:
    A researcher has added 2.06 g of the salt sodium nitrate to a cylinder containing water. The cylinder diameter is 2 inches and the depth of the water in the cylinder is 4 inches. Determine the concentration of salt in solution, showing your answer in the units specified.
    Sodium Nitrate = 85 g/mole
    Density of water = 1 g/ml
    mg/L
    mass %
    molarity
Part 7: Environmental Engineering Calculations

## Slide 27: ENGR 1111 Intro to Engineering: Civil Engineering Fall 2022 Part 7: Environmental Engineering Calculations